## Slide 1: Status of Existing Instruments Subaru Users’ Meeting 2010
Hiroshi TERADA
(Science Operation Division)

## Slide 2: Highlight (2010-2011)
2010 May
  FMOS joined in the lineup
  IRS1 low-resolution only
  IRS2 will come in S11A.
2011 May
  LGS AO188 will start open use.
  Evaluation on-going
IRCS
HiCIAO
AO188
HDS
FOCAS
MOIRCS
COMICS
FMOS
S-Cam
Instruments Lineup
Hiroshi TERADA @ Subaru Telescope
Subaru 2010UM
NsIR
NsOpt
PF
Cs

## Slide 3: Highlight (Downtime)
To keep functional,
Chart: 
| S03A | S03B | S04A | S04B | S05A | S05B | S06A | S06B | S07A | S07B | S08A | S08B | S09A
観測時間 | 85475 | 98420 | 88735 | 100833 | 79439 | 77467 | 71915 | 83084 | 87284 | 81734 | 88559 | 94863 | 78701
望遠鏡トラブル | 2557 | 4080 | 2513 | 2153 | 1102 | 4724 | 1333 | 1134 | 1883 | 1588 | 2002 | 1927 | 1734
装置トラブル | 871 | 1048 | 2221 | 1847 | 2606 | 1378 | 661 | 1365 | 2486 | 2245 | 822 | 671 | 283
ソフトウエアトラブル | 39 | 234 | 174 | 133 | 180 | 173 | 132 | 127 | 494 | 599 | 72 | 279 | 25
蒸着・地震・他 | 8100 | 0 | 0 | 0 | 0 | 0 | 3990 | 11015 | 0 | 0 | 0 | 0 | 580
■ Instrument trouble time
Less
trouble!!
Operating Efficiency
Semester
In 2009 UM
Subaru 2010UM
Hiroshi TERADA @ Subaru Telescope
Chart: 
| S03A | S03B | S04A | S04B | S05A | S05B | S06A | S06B | S07A | S07B | S08A | S08B | S09A | S09B | S10A
Instrument Down Time | 0.97929 | 1.0098 | 2.3718 | 1.7596 | 3.1274 | 1.6455 | 0.89275 | 1.5926 | 2.6979 | 2.6054 | 0.8988 | 0.68652 | 0.45938 | 0.91093 | 0.70009
Still functioning well
(%)
Instrument Downtime

## Slide 4: Executive Summary
MOIRCS
  Channel-1 trouble and recovery, and New NBF and ND
FOCAS
  FDCCD upgrade
HDS
  Image-slicer => Tajitsu-san’s Poster
Suprime-Cam
  1-Channel signal anomaly, on-site DA system, and New NBFs Grisms
AO188+IRCS
  DM failure and recovery, and NGS resumed.
  LGS development (=> Hayano-san’s Talk) and Open in S11A.
FMOS
  IRS1(LR) open use and HR, IRS2 development => Tamura-san’s talk
Gen2
  Most of the operations (except for S-Cam) are conducted using Gen2.
To keep operational and competitive,
Subaru 2010UM
Hiroshi TERADA @ Subaru Telescope

## Slide 5
Recognized on Sep. 28, 2010 (before the first S10B obs.).
Channel-2 side only Operation during the whole S10B.
  2 N (Keck[te]), 2 N (Gemini[te]), 1 N (UH), 4 N (Subaru OpenUse[ip])
    [te]: Time Exchange Program, [ip]: Intensive Program
One month troubleshooting went fairly well.
  Fixed within Dec., 2010, and will be verified in Jan., 2011.
Cause – stack of bad screws used in one holder for new grism.
Good guy.
BAD guy (longer by just 1mm…).
MOIRCS (Channel-1 turret-rotation trouble)
Subaru 2010UM
Hiroshi TERADA @ Subaru Telescope

## Slide 6
Br γ (cw/bw = 2.163/0.025 mm) now available.
ND filter become available.
  Main purpose is to provide good-quality Ks-band Dome flats
  (but can be used to scientific data acquisition).
Chart: BrGamma 2166/25nm BARR ED858-2/3 5 degrees AOI, 120 K condition (approx.) 298K, 0O AOI: PeakT%=92%; CWL= 2163nm; BW= 25nm
MOIRCS (New Filters)
Subaru 2010UM
Hiroshi TERADA @ Subaru Telescope

## Slide 7
Engineering Obs: June 2010
Open use : from Oct. 2010
Improvements on
  higher efficiency,
  less fringing,
  faster readout,
  better cosmetics
    (only 1 dead column in 2 CCDs)
However, please note..
  extensive cosmicrays
  wider CCD gap (50→70pixel)
FOCAS (CCD Upgrade)
Total Efficiency (compared to the MIT CCD)
~0.9@400nm, ~1.3@500nm, ~2@1000nm
Subaru 2010UM
Hiroshi TERADA @ Subaru Telescope

## Slide 8
Less fringing
Hamamatsu
MIT
Wavelength (nm)
domeflat with 0".8+300R+O58
FOCAS (CCD Upgrade)
Subaru 2010UM
Hiroshi TERADA @ Subaru Telescope

## Slide 9
Lyα
NV
OI/SiII
CFHQS J0210-0456 (z=6.44)
CFHQS J2329-0301 (z=6.42)
Flux (erg s-1 cm-2 Å-1)
Wavelength (Å)
VPH900 (7500-10500Å, R~2000, ~2hours)
FOCAS (CCD Upgrade)
Performance Demonstration (high-z QSOs)
Subaru 2010UM
Hiroshi TERADA @ Subaru Telescope

## Slide 10: HDS (Image-Slicer upgrade)
=> Please see Tajitsu-san’s poster for details.
Slicing Φ1”.5 image into
  0”.3 x 5 spectra
R=110,000
  (slit width of 0”.3)
Engineering Obs:
  Jun. and Dec., 2010
1.8 times higher efficiency confirmed!
  (under 0”.68 seeing)
Subaru 2010UM
Hiroshi TERADA @ Subaru Telescope

## Slide 11: Suprime-Cam
Signal at 1-channel of 1 CCD (DET-ID:9)
  Found on Sep. 17, 2010
  After adjusting offset voltage,
    operation has been okay (since Oct., 2010)
  Please note that gain was changed
    on the channel.
On-site data analysis system available
  Operation since Mar., 2010
    Data assurance can be done on site
    (Seeing, sky level,… etc.)
Analysis pipeline (SDFRED2) released
  For the data obtained after 2008/07.
  (http://www.naoj.org/Observing/Instruments/SCam/sdfred/)
DET-ID:9
g’-band domeflat
Jun.,2010
Oct.,2010
Screenshot of On-site data analysis
Subaru 2010UM
Hiroshi TERADA @ Subaru Telescope

## Slide 12: Suprime-Cam (New Filters and Grisms)
Narrow band filter Open
  N-A-L656 (Hα): S10B~
  W-A-Y (Y-band): S11A~
Grisms will be Open
  Planning in 2011
GrismB
GrismR
N-A-L656
W-A-Y
Subaru 2010UM
Hiroshi TERADA @ Subaru Telescope
Notes: 1. N-A-L656 filter (Halpha filter) の公開 2009 年 8 月に試験観測データを取得済み。S10B から公開する予定。 有効波長 6568A, FWHM 約140A。
res_na656.pdf : NA656 filter の透過率
N6820NE2.png : 試験観測で撮られた散光星雲 NGC6820 北東部領域の画像 赤いところが Hαで明るいところ (B, R, NA656 の合成)
M27s0.png : 試験観測で撮られた亜鈴星雲 M27 の画像 赤いところが Hαで明るいところ (B, R, NA656 の合成) 合成画像は八木さんにより作成されたもの。
2. Suprime-Cam 観測支援用オンサイトデータ解析システム の本格運用 古澤さん及び天文データセンター研究員の大倉さんが中心に開発を進めている。
ハワイ側では SS の仲田が参加し、Suprime-Cam 観測の運用効率向上を 目指している。
このシステムにより、Suprime-Cam 観測データ取得後ただちに1次解析が行われ、 データの品質を評価するための基本的な情報 (Seeing, sky level など) が 得られる。

## Slide 13: Failure and Recovery of DM
AO188+IRCS (NGS mode)
Occurred on Jan. 27, 2010
  (during LGS Engineering run)
Recovered in late Oct., 2011
13N Backup Programs selected by TAC
4N  IRCS (w/o AO188) Obs.
Red: H2(1-0) 2.122μm, Green: Brγ 2.167μm, Blue: [FeII] 1.644μm
50”x 63”
Subaru 2010UM
Hiroshi TERADA @ Subaru Telescope
IRCS 52mas Camera

## Slide 14: Performance w/ New DM
Confirmed that AO188 performance with new DM is almost same as before its failure.
Resumed OpenUse since Nov., 2010.
Points w/o circle: before DM failure
Points w/ circle: after DM replacement
AO188+IRCS (NGS mode)
Subaru 2010UM
Hiroshi TERADA @ Subaru Telescope

## Slide 15: Successful Closed Loop using Laser Guide Star
Obtained diffraction-limited PSF w/ LGS
Will start OpenUse from May 2011.
  Testing is underway..
Seeing (FWHM ~ 0”.3)
LGS mode w/R14mag TT GS (SR~0.2 FWHM ~ 0”.08)
AO188+IRCS (LGS mode)
IRCS 20mas Camera
=> Please tune in Hayano-san’s talk
Subaru 2010UM
Hiroshi TERADA @ Subaru Telescope

## Slide 16: Operations of Existing Instruments
We appreciate your kind cooperation about
  Pre-imaging (30min; FOCAS and 1hour; MOIRCS), and
  Clear information on MOIRCS MOS masks and S-Cam filters
  We look forward to your continued support for these.
First generation instrument: (>10yrs old)
  Some parts: ~15 yrs old…
Still succeeding in keeping in good shape
  Thanks to dedicated works by support staff
  Once serious trouble occurs, huge resources are required.
Serious investigation required for the “future” of “Existing instruments” upon ‘Users’’ demands.
  Especially in consideration of the future instrumentation in Subaru.
Subaru 2010UM
Hiroshi TERADA @ Subaru Telescope

## Slide 18: (Complex) Operation Progress
AO188+IRCS (NGS mode)
Most of NGS commands can be executed from OCS side
Efficient parameter tuning realized
ADI, Non-sidereal, Parallactic angle spec. ready.
NGS parameter tuning (gain scanning)
=> LGS operation could be even more complicated…
Subaru 2010UM
Hiroshi TERADA @ Subaru Telescope

## Slide 19
AO188+IRCS (DM resume)
Gemini
LGS Altair+NIRI
63”x 63”
9”.6x 14”.5
H2(1-0)
IRCS 52mas Camera
Red: H2(1-0) 2.122μm, Green: Brγ 2.167μm, Blue: [FeII] 1.644μm
H2(1-0)
[FeII]
[FeII]
Subaru 2010UM
Hiroshi TERADA @ Subaru Telescope